## Slide 1: Adaptive Bit Rate
  Doug Keltz
  Doug.Keltz@Tektronix.com
  678-296-5073

## Slide 2: Why Adaptive Bitrate Streaming?
Consumers expect content
everywhere and on anything
they own.
How do we accomplish this?

## Slide 3: What is Adaptive Bitrate Streaming ?
Deliver content to a variety of device types
Bandwidth is the unknown factor
The client side player determines available bit rate and requests the appropriate content to meet current bandwidth availability
Streams are setup to “adapt” to available bandwidth
As client side bandwidth availability changes, quality can increase or decrease. All the while, continuously delivering content

## Slide 4: The Shift to HTTP-Based Delivery
There is now something of shift away from classic streaming protocols towards HTTP
HTTP-based media delivery has little to no firewall restrictions because firewalls and routers regularly pass HTTP through port 80
HTTP media delivery doesn't require special proxies or caches. An ABR file is just like any other file to a web cache server
Networking equipment also doesn’t need to know/understand video. It sees ABR traffic as simple web activity.

## Slide 5: What Adaptive Streaming Technologies are available ?
There are two fundamental types of adaptive streaming technologies available
  Non-segmented/fragmented such as H.264/SVC (Scalable Video CODEC)
  Segmented/Fragmented such as
    Apple Live Streaming (HLS) - most popular
    Microsoft Smooth Streaming
    Adobe Flash Dynamic Streaming - least popular
    DASH - new unified standard
Most operators are adopting segmented/fragmented adaptive streaming technologies – primarily HLS with plans to move to DASH
A few operators are hedging by offering streams using two or three major segmented/fragmented technologies
Notes: DASH is new unifying standard to pontially replace existing standards but for now they can all work using DASH
Apple is every 10 seconds
Adobe and MS is every Two Seconds

## Slide 6: Segmented/Fragmented
Files must be “fragmentable”
  H.264 video needs periodic IDR (Instantaneous Decoder Refresh) frames
  No frame after an IDR frame can reference any frame before it
  Each fragment must begin with an IDR frame
Unacceptable picture quality for lower bitrates
  Blockiness and other compression artifacts reduce the perceptual video quality of the program content
  Picture Quality Analysis tools can be used to “tune” the encoder to the best possible quality for a given target bitrate
IDR
P
B
I
Notes: IDR B B P B B I

## Slide 7
DASH is a standard for adaptive streaming over HTTP that has the potential to replace existing proprietary technologies like Microsoft Smooth Streaming, Adobe Dynamic Streaming, and Apple HTTP Live Streaming (HLS).
Unified standard would be a boon to content publishers, who could produce one set of files that play on all DASH-compatible devices.
Other advantages
  Codec-independent
  Does not specify a DRM method (supports all DRM techniques specified in ISO/IEC 23001-7: Common Encryption)
  Trick modes for seeking, fast forwards and rewind
  Dynamic advertising insertion
MPEG DASH - Dynamic Adaptive Streaming over HTTP
Notes: IDR- like I frame to clear buffer and not look beyond this frame. Instantaneous Decoder Refresh
DRM = Digital Right Management
Manifest files track what is in file.

## Slide 9: Linear Adaptive Streaming Simplified Architecture
Transcoders
Fragmenters
(Apple, MS, Adobe)
Origin Server
Master
Encoders
Multiple copies at different bit rates (1-16 copies)
Same content split in to small 2 to 10 sec. files (fragments)
Notes: Apple is every 10 seconds
Adobe and MS is every Two Seconds

## Slide 10: ABR Profiles
Video Transcoding
Transcode the input to each required output profile – where a given profile will have its own resolution and bit rate parameters – including scaling to resolutions suitable for each client device.
Because the quality of experience of the client depends on having a number of different profiles, it is necessary to encode a significant number of output profiles for each input. Deployments may use anywhere from 4 to 16 output profiles per input.
 | Width | Height | Bit rate | 
 | 1280 | 720 | 3 Mbps | 
 | 960 | 540 | 1.5 Mbps | 
 | 864 | 486 | 1.25 Mbps | 
 | 640 | 360 | 1.0 Mbps | 
 | 640 | 360 | 750 Kbps | 
 | 416 | 240 | 500 Kbps | 
 | 320 | 180 | 350 Kbps | 
 | 320 | 180 | 150 Kbps | 

## Slide 11: Example Profile Bit Rates by Device Type

## Slide 12: Walk me through the initial process
Customer Client
Content Proxy
Edge Cache
Hello! Here is my sub id, device type, bandwidth available, session ID.
I would like Superman 3, please.
Sub id, device type, bandwidth available, and session ID would like Superman 3, please
Authentication
Origin Cache
Yes
Do I have the asset?
No
Send manifest file (XML)
Profile 2 of Superman 3, to session ID, please
Profile 2 of Superman 3, to session ID, please
Process manifest file
Request asset file
Transfer file to Edge Cache
Transfer file segment
Here is your file, enjoy
Here is your file, enjoy
Measure download speed and begin playback

## Slide 13: What happens with available bandwidth changes?
Customer Client
Content Proxy
Edge Cache
Origin Cache
Measure download speed from last file
Examine manifest file and determine best profile
Here is my session ID.
Profile 6 of Superman 3, please
Profile 6 of Superman 3, to session ID, please
Transfer file segment
Here is your file, enjoy
Here is your file, enjoy
Measure download speed from last file
Examine manifest file and determine best profile
Repeat process until asset is finished or customer stops playback

## Slide 14: Sentry Multi-Screen Video Network Quality Assurance
Live or VOD Content
Transcode
Fragment & DRM
Origin Server
Smartphone
Tablet
Computer
TV
Video Monitoring
Over HTTP
Element Mgmt. Control,
& Roll-up report
ABR Video Preparation
ABR Video Distribution
Video Monitoring
Over UDP/RTP
Video Monitoring
Over UDP/RTP
CDN
Sentry
Sentry
Sentry ABR
Sentry ABR
Medius
Video Monitoring
Over HTTP
QoE – Decodeability
PVQ - Artifacts
Audio Loudness
SCTE35
QoE – Decodeability
PVQ - Artifacts
Audio Loudness
EBP/IDR – Q4
Profile availability
Packet strucutre
Packet rate
Manifest file verification

## Slide 15: Network and Troubleshooting Overview

## Slide 16
MTS-4000
Source Content
Receiving
Video Processing
Sentry
Sentry
Sentry Edge II
Medius
iPad
Smartphone
Computer
TV
IP Transport
Sentry
Sentry Verify
Linear or VOD
TS over
RF/IP/ASI
Modulation
HFC
Access Network
CDN, Last Mile
Video Processing
Sentry
Sentry Verify
Muxing
Splicing
Rate-Shaping
QAM
Where to Monitor and Test
Transcoding
Muxing
Rate-Shaping
(Encrypt)
1G or 10G
Optical/Copper
WFM-5250
Notes: 16

## Slide 17
What to Monitor
Operational Concerns
IP Network Performance
TS Performance
Audio Level Compliance

## Slide 18
What to Monitor
Customer Impacting Issues
Video Freeze / Black
Audio Silence
Blocking / Tiling (Video QOE)
Blurred / Soft Picture
(Preceptual Quality)
Program Unavailable

## Slide 19
Troubleshooting video signals in a broadcast or cable facility requires the use of an MPEG Analyzer that provides multiple input signals all running in parallel.
Critical capabilities in an MPEG Analyzer should include:
Transport stream generation, modification and analysis
  Real and deferred time
  Including MPEG-2, H.264 & MPEG-4 AAC
  Multiplexer
  Automatic error triggered recording and capture
A range of physical interfaces
  Multi-port ASI
  RF (DVB-S2, 8-VSB & QAM-B)
  Video over IP analysis and generation (1G and 10G)
Comprehensive suite of software tools for analyzing all layers of video
  High accuracy RF layer analysis
  Transport, Program & Elementary Streams
  Video & Audio Quality of Experience (QoE)
  Picture Quality
Troubleshooting
Notes: Troubleshooting video signals in a broadcast or cable facility requires the use of an MPEG Analyzer that provides multiple input signals all running in parallel.
Critical capabilities in an MPEG Analyzer should include:
Transport stream generation, modification and analysis
  Real and deferred time
  Including MPEG-2, H.264 & MPEG-4 AAC
  Multiplexer
  Automatic error triggered recording and capture
A range of physical interfaces
  Multi-port ASI
  RF (DVB-S2, 8-VSB & QAM-B)
  Video over IP analysis and generation (1G and 10G)
Comprehensive suite of software tools for analyzing all layers of video
  High accuracy RF layer analysis
  Transport, Program & Elementary Streams
  Video & Audio Quality of Experience (QoE)
  Picture Quality

## Slide 20
Quality of Service (QOS)
IP
Small
Inter-Packet Gap
Decoder
Monitor, TV, etc
Buffer
(Removes Ethernet frame and buffers MPEG)
MPEG
Inter-Packet Gap
MPEG Packets
Buffer Over-Run
Key Measure – Dropped Packets
  IP switches can occasionally drop packets.
  Most video over IP uses UDP (no retransmission)
  With MPEG-2 transport packets, continuity counters help identify dropped packets.
  Counting lost packets at the IP layer is not too helpful as each missing packet will usually generate audio or video degradation.
Notes: IP Video Key Measures – Dropped Packets
  Given the complexity of IP switches, occasional failures or overloads do occur and cause IP packets to get dropped.
  Most video over IP uses UDP (send and forget) – so we need another method to know when an IP packet has been lost.
With MPEG-2 transport packets, each TV program includes separate 4-bit counters for each audio and video element, so it is possible to determine when a packet might have been dropped.
  Calculating the ratio of missing packets to total packets is possible, but not too helpful as each missing packet will usually generate audio or video degradation.

## Slide 21: Quality of Experience (QOE)
Compressed Video is not “linear” because different frames have different importance and an error in an I-frame may reside on the TV screen for an entire Group of Pictures (about 500 ms).
With a bad B-frame picture, it only stays on the TV screen for one frame (1/30th or 1/25th of a second).
A bad bit could cause an entire slice or row of pixels to turn green.
I
B
B
B
P
B
B
B
P
B
B
B
P
B
B
B
P
No Errors
Slice Error
Major Errors Caused
By Corruption of Following
I-Frame
Notes: To measure the QoS of the MPEG-2 transports, TR 101 290 is sufficient.
Determining the quality of the audio and video (QoE) will require much more processing than simply looking at MPEG transport packet headers and packet gaps.
Given that compressed TV is not linear like uncompressed audio, a bad bit landing in the middle of an MPEG video I-frame is much worse than a bad bit landing in the corner of a B-frame.
The reason that this issue is not considered linear is because an error in an I-frame may reside on the TV screen for an entire Group of Pictures (about 500 ms).
With a bad B-frame picture, it only stays on the TV screen for one frame (1/30th or 1/25th of a second).
Also, a bad bit could cause an entire slice or row of pixels to turn green. Or maybe the bad bit only causes a signal pixel to change color.
We need to keep track of impairments within each audio and video element.

## Slide 22: QOE Reason codes
Missing Video Slice
  A particular video slice (horizontal row of macroblocks) was expected but not found. A special case of Video Syntax Error
Unexpected Video Header
  The state following the decode of a video header was unexpected. Special case of Video Syntax Error.
Video Syntax Error
  An unexpected state occurred while decoding video slice data.
Video Packet Loss
  A Continuity Count error (a.k.a., discontinuity) is detected at the same time there is a video PID bitrate dropout of a short duration (< 200 ms)
Video PID Dropout
  A long video PID bitrate dropout occurred (> 200 ms). (may or may not be accompanied by a CC error, see "Note 2" for details.)
Video Buffer Underrun
  A video frame's DTS value was >= the current PCR resulting in a (decode) buffer underrun.
Video Buffer Overrun
  A video frame's DTS value was > 3 seconds for MPEG-2 or > 5 seconds for H.264 behind the current PCR resulting in a decode buffer overrun.
Compression artifacts inclusion
  When PVQ score reduced by 20% or more in 5 seconds

## Slide 23: QOE or PVQ
Picture
Slice
Macroblock
Block
QoE =
MPEG structural errors
PVQ =
Compression artifacts
.
.
.
Group Of Pictures
Video PID (MPEG packet)

## Slide 24: Troubleshooting Examples

## Slide 25: Buffer Underrun Issue
Playback of captured video shows blocking around the head if image.
Problem: Customer complaining about blocking and tiling. Operations receiving QOE Alerts.

## Slide 26: Buffer Under run Issue
Problem: Customer complaining about blocking and tiling. Operations receiving QOE Alerts.
Sentry shows low QOE Score (70) and identifies the issue as Buffer Under run.

## Slide 27: Buffer Under run Issue
Analysis with the MTS-4000 (TSCA Software) shows PTS-PCR going below 0 (under run).
Under normal operation the PTS-PCR variation should never go below 0. Anytime 0 is reached or negatively exceeded then there is a buffer underrun condition which can cause problems.
Re-grooming the mux corrected the problem.
Problem: Customer complaining about blocking and tiling. Operations receiving QOE Alerts.

## Slide 28: Transport Packet Header
Sync Byte 8
Transport Error Indicator 1
Start Indicator 1
Transport Priority 1
PID 13
Scrambling Control 2
Adaptation Field Control 2
Continuity Counter 4
Adaption Field
Payload
Header Payload
188 Bytes
Adaptation Field Length 8
Discontinuity Indicator 1
Random Access
Indicator
1
Elem Stream Priority Indicator
1
5 Flags
5
Optional Fields
Stuffing Bytes
OPCR 48
Splice Countdown 8
Transport Private Data
Adaption Field Extension
PCR 48
Minimum 4-byte header
Discontinuity Issue
Notes: Each transport packet has a minimum 4-byte header and a maximum 184-byte payload,
Key data in the minimum header are the Sync Byte and the PID (packet identification).
PID values are 13 bits giving them a range of 0 to 8191. Only 0, 1, and 8191 are assigned by the MPEG standard.
Program timing information is carried by the PCR (program clock reference) which is in the optional fields of the adaptation field of some transport packets.
Some other fields of interest:
continuity_counter: a 4 bit field that counts through 16 values on a “per-pid” basis. Discontinuities are only allowed in particular situations. This field is used to determine lost or repeated packets.
discontinuity_indicator: indicates both a timebase discontinuity and a continuity counter discontinuity.
random_access_indicator: indicates that the next PES packet to start in this PID stream contains a video sequence header or the first byte of an audio frame.
splice_countdown: an 8 bit field specifying the number of packets, of the same PID value, before a splice point. Hence, a splice point is reached when this field has a value of 0. This packet contains the last coded byte of a picture or audio frame. The next TP of the same PID must contain the start of a new PES packet and that PES packet payload must begin with a video sequence header or the start of an audio frame.

## Slide 29: Discontinuity Issue
Capture played back shows blocking across top of screen.
Problem: Customer complained about continuous tiling for program.

## Slide 30: Discontinuity Issue
Monitoring system alerted on low QOE score due to ‘Video Packet Loss’.
Problem: Customer complained about continuous tiling for program.

## Slide 31: Discontinuity Issue
Looking at the Transport Stream Status View, we see all programs are experiencing Discontinuities.
Problem: Customer complained about continuous tiling for program.

## Slide 32: Discontinuity Issue
Analysis with the MTS-4000 (TSCA Software) shows continuous Discontinuity for Video PID.
Problem: Customer complained about continuous tiling for program.

## Slide 33: Discontinuity Issue
Analysis with the MTS-4000 (TSCA Software) shows continuous Discontinuity for Video PID, drilling into the packet view shows missing packet (12).
Problem: Customer complained about continuous tiling for program.

## Slide 34: Discontinuity Issue
ESPN1
ESPN2
MCR
Presentation Control
Transcode
Web Server
VoD Server
Browse/Lo-Res
Proxy
Telecom/3GPP
Provider
Local Content and Ads
HD Encode
SD Encode
Edit
Metadata
Graphics
Content Processing
Central
Storage
Ingest
Content
Grooming
SD-SDI, HD-SDI, 3G-SDI
ASI, IP, RF
Monitoring Need:
Video errors and compliance
Audio errors and compliance
Audio Loudness
Closed Caption and Metadata Errors
Monitoring Need:
Encoder quality
Post mux video and audio QoE
IP and TS structure errors
Splicing, EBI, tru2way Errors
Filebased Formats
Monitoring:
Video QoE and Video Codec Errors
Audio QoE and Audio Codec Errors
File Wrapper structure
Loudness monitoring and correction
Splice, Encrypt
Modulate
Adaptive Bit Rates and Streaming
Monitoring:
Profile availability
Packet structure
Packet rate
Manifest file verification

## Slide 35: CALM Act Issue
Problem: Customer complained loud commercials.

## Slide 36: CALM Compliance
Circled area represents entire Ad segment. The entire graph represents a 15 minute of time. The thumbnail to the left represents the current active content. Leading into the commercial, the program content had the same type of level changes.
Problem: Customer complained loud commercials.

## Slide 37: CALM Compliance
Initial transition into a broadcast (non-adcue) commercial. Ballgame being advertised. Dialnorm at -31 actual audio at -24. Each column/block represents 30 seconds.
Problem: Customer complained loud commercials.

## Slide 38: CALM Compliance
Second (non-adcue) commercial. Cash for Gold being advertised. Dialnorm at -31 actual audio at -24 as with first commercial. Each column/block represents 30 seconds.
Problem: Customer complained loud commercials.

## Slide 39: CALM Compliance
Third (non-adcue) commercial. Cal Ripken being advertised. Dialnorm at -31 actual audio at -24 as with first commercial. Each column/block represents 30 seconds.
Problem: Customer complained loud commercials.

## Slide 40: Doug.Keltz@Tektronix.com 678-296-5073